*** Settings ***
Metadata	Version	1.0
...	More Info	For more information about Robot Framework see http://robotframework.org
...	Author	Payal Jain
...	Date	19 Dec 2016
...	Executed At	${HOST}
...	Test Framework	Robot Framework Python
Documentation	A test suite with tests for configuring BGP.
...	Topology:-
...	__________________________
...	|	|
        | R1 AS2	|
...	|	/ \	|
...	| / \	|
...	| R2 R3	|
...	|	|	|	|
|__________	|_____|__________|
__________ |	|__________
...	| AS1	|	| AS3	|
|	|	|	|
...	| R4	|	| R5	|
...	|__________	|	|__________	|
...	Testplan Goals:-
...	1. Configure IP addresses as per the topology.
...	2. Each Router should have a loopback0 interface.
...	3. Configure OSPF within AS2 to advertise the loopback0 interfaces.
...	Don't advertise or run OSPF on the links interconnecting AS1 and AS3.
...	4. Configure IBGP between R2 and R3. Source the BGP updates from the loopback0 interfaces.
...	5. Enable BGP synchronisation.
...	6. Configure EBGP between R2 and R4.
...	7. Configure EBGP between R3 and R5.
...	8. Advertise the loopback0 interfaces on R4 and R5.
...	9. Ensure AS1 and AS3 can communicate with each other without removing the BGP synchronisation command.
Resource	Resource.robot
Suite Setup	Setup Actions
Suite Teardown Teardown Actions

---
*** Test Cases ***
Bring_up Phase
Configure IP addresses as per the topology
   Configure ip address
   Set loopback interface
    Configure OSPF within AS2 to advertise the connected networks
   Enable OSPF in devices present in AS2 and set the ospf neighbors
    Configure IBGP and source the BGP updates from the loopback0 interfaces
   Enable BGP and advertise the updates from the loopback interface
    Enable BGP Synchronisation
   Enable synchronisation between border routers
    Configure EBGP
   Enable BGP and advertise networks connected outside the autonomous system
    Advertise the loopback interface
   Advertise loopback interface on AS1 and AS3